## Slide 2: CHAPTER 10 Error Detection and Correction
4-1

## Slide 3
Data can be corrupted during transmission.
  Some applications require that errors be detected and corrected.
Error detection and correction are implemented either at the data link layer or the transport
layer of the OSI model.

## Slide 4: Data Link Layer

## Slide 6
Single-bit error
In a single-bit error, only 1 bit in the data unit has changed.

## Slide 7: Multiple-bit error

## Slide 8: Burst Error

## Slide 9
Redundancy
The central concept in detecting or correcting errors is redundancy
To detect or correct errors, we need to send extra (redundant) bits with data

## Slide 10: Error Detection
In error detection, we are looking only to see if any error has occurred. The answer is a simple yes or no. We are not even interested in the number of errors.

## Slide 12: Vertical Redundancy Check
VRC called a Parity Check
A parity bit is added to every data unit
Even-parity checking or odd-parity checking

## Slide 13: Example
Sender wants to send “world” In ASCII, the five characters are coded as:
1110111 | w 1110111 0
1101111 | o 1101111 0
1110010 | r 1110010 0
1101100 | l 1101100 0
1100100 | d 1100100 1

## Slide 14
1110111 | w | 1111111 0 | 7
1101111 | o | 1101111 0 | 6
1110010 | r | 1110110 0 | 5
1101100 | l | 1101100 0 | 4
1100100 | d | 1100100 1 | 4
Receiver counts the 1’s and rejects it because of Odd parity generator
Receiver Side
Suppose “world” is received by the receiver corrupted:

## Slide 15: Performance of VRC
VRC can check all single-bit errors
It can not detect errors if the total number of errors is even
We have an Even Parity data unit where the total number of 1’s including the parity bit is ‘6’ : 1000111011
If 3 bits change value resulting parity will be odd and an error will be detected: 1111111011: 1’s = 9
VRC cannot detect errors when the total number of bits changed are even

## Slide 16: Longitudinal Redundancy Check
A block of bits is divided into rows and a redundant row of bits is added to the whole block

## Slide 17: Example
Sender Side
Suppose the following block is sent:
1 0 1 0 1 0 0 1
0 0 1 1 1 0 0 1
1 1 0 1 1 1 0 1
1 1 1 0 0 1 1 1
1 0 1 0 1 0 1 0 (LRC)

## Slide 18: At the Receiver Side
Receiver checks LRC, some of bits do not follow even parity rule and whole block is discarded
10100011
10001001
11011101
11100111
10101010 (LRC)

## Slide 19: Cyclic Redundancy Check
Uses binary division

## Slide 21: Performance of CRC
CRC can detect all burst errors
CRC can detect with a very high probability burst errors of length greater than the degree of the polynomial

## Slide 22: Polynomial and Divisor

## Slide 23: Standard Polynomials

## Slide 24: Checksum
Error detection method used by the higher layers
All sections are added and complemented to get the checksum, using one’s complement arithmetic

## Slide 25
Performance of Checksum
Detects all errors involving an odd number of bits
Detects most errors involving an even number of bits
One pattern remains elusive
10101001
Suppose a block of 16 bits need to be sent: 00111001
10101001
00111001
----------------
11100010 Sum
00011101 Checksum Sent pattern:
10101001 00111001 00011101
checksum

## Slide 26: Hamming Code

## Slide 27: Hamming Code

## Slide 28: Redundant Bit Calculation

## Slide 31: Example: Correcting Error
Receiver receives 10010100101

## Slide 32
Thank you