## Slide 2
Chapter 4. Digital Transmission
4-1

## Slide 3
Digital-to-digital conversion
How to represents digital data by using digital
signals.
Three techniques used in the conversion
 Line coding
 Block coding
 Scrambling

## Slide 4: Line Coding
Line coding is the process of converting digital data to digital signals.
Data (text, numbers, graphical image, audio, video etc) are store d in computer memory as sequence of bits.
Line coding converts a sequence of bits to a digital signal.
At the sender, digital data are encoded into digital signal; at the receiver, the data are recreated by decoding the digital signal.

## Slide 5
Line coding scheme can be divided into five broad categories :
Line Coding

## Slide 6: Unipolar Scheme
In a unipolar scheme, all the signal levels are on one side of the tim e axis; either above or below.
NRZ (Non-Return-to-Zero) scheme
Designed so that positive voltage defines bit 1 and the zero voltage defines bit 0.
It is called NRZ because the signal does not return to zero at the middle of the bit.

## Slide 7: Polar Scheme
In a polar scheme, the voltages are on both sides of the time axis.

## Slide 8
NRZ
NRZ-L (Non Return to Zero-Level) – Level of signal depends on the type of bit it represent
s. A positive voltage means

## Slide 9
NRZ-I

## Slide 10: Polar Scheme : RZ
Signal changes during each bit
Uses Three values (+, -, 0) are used
– Bit 1: positive-to-zero transition, bit 0: negative-to-zero transition

## Slide 11: Polar Scheme : Biphase
Combination of RZ and NRZ-L/NRZ-I ideas
Signal transition at the middle of the bit is used for synchronization
Manchester (combine RZ & NRZ-L)
  Bit 1: negative-to-positive transition
  Bit 0: positive-to-negative transition
Differential Manchester (combine RZ & NRZ-I)
  Bit 1: no transition at the beginning of a bit
  Bit 0: transition at the beginning of a bit

## Slide 12: Bipolar Scheme
Three levels of voltage, called “multilevel binary”
Bit 0: zero voltage, bit 1: alternating +1/-1
AMI (Alternate Mark Inversion) and pseudoternary
– No DC component

## Slide 13: Block Coding
Block coding is a error control coding
To ensure accuracy of received data redunt bi ts are used
The decoder uses the redundant symbols to d etect and possibly correct whatever errors occ urred during transmission.

## Slide 14: Block Coding

## Slide 15
Scrambling
However long 0s upset the synchronization and not suitable for long distance.
Looking for a solution – a technique that does not increase t he number of bits and providing synchronization.

## Slide 16
Analog-To-Digital Conversion
Analog information (e.g., voice) → digital signal (e.g., 10001011…)
Two techniques :
  Pulse Code Modulation (PCM)
  Delta Modulation

## Slide 17
Pulse Code Modulation (PCM)
Three processes :
  The analog signal is sampled
  The sampled signal is quantized
  The quantized values are encoded as streams of bits

## Slide 18: Pulse Code Modulation (PCM)
Sampling
The first step in PCM is sampling. The analog si gnal is sampled every Ts, where Ts is the sampl e interval or period

## Slide 19
Pulse Code Modulation (PCM)
Quantization (Examples)
– Quantization is the process of converting a continuous range of values into a finite range of discreet values.

## Slide 20
Pulse Code Modulation (PCM)
Encoding
After each sample is quantized and the number of bits per sample is decided, each sample is change d to an nb-bit codeword.
If the number of quantization levels is L, the num ber of bits is nb = log2L.
In Above Figure the encoded words are shown in
Bit rate = sampling rate × number of bits per sample = fs × n b
the last row. A quantization code of 2 is encoded as 010; 5 is encoded as 101; and so on
The bit rate can be found as
–

## Slide 21: Delta Modulation
PCM is a very complex technique. Other techniques have been developed to reduce the complexity of PCM. The simplest is delta modulation

## Slide 22: Delta Modulation
Modulator
The modulator is used at the sender site to create a stream of bits from an analog signal.
The process records the small positive or negative changes, called delta O.
If the delta is
positive, the process records a I; if it is negative, the process records a O

## Slide 23
Delta Modulation
Modulator
  The output of the comparator also makes the staircase itself; if the next bit is 1, the staircase maker moves the last point of the staircase signal δup, otherwise moves th e δdown.
  A delay unit is used to hold the staircase function for a period between two compari sons.

## Slide 24
Delta Modulation
Demodulator
  The demodulator takes the digital data, and using the staircase maker and the delay unit, creates the analog signal.
  A low-pass filter is used to smoothen the signal.

## Slide 25
TRANSMISSION MODES
primary concern when we are communicating is the data stream. Do we send 1 bit at a time; or do we s end group of bits.

## Slide 26: TRANSMISSION MODES
Parallel Transmission
The mechanism for parallel transmission is a con ceptually simple one: Use n wires to send n bits at one time. That way each bit has its own wire, and all n bits of one group can be transmitted fr om one device to another

## Slide 27
TRANSMISSION MODES
Serial Transmission
In serial transmission one bit follows another, so we need only one communication channel rather than n to transmit data between two communica ting devices

## Slide 28: Serial Transmission
Synchronous Transmission
In synchronous transmission, we send bits one after another without start or stop bits or gaps.

## Slide 29: Serial Transmission
ASynchronous Transmission
In asynchronous transmission, we send 1 start bit
(0) at the beginning and 1 or more
stop bits (Is) at the end of each byte. There may be a gap between each byte.

## Slide 30
Thank you