## Slide 1
Department of Computer Science PAF-KIET North Campus
Data Communication and Computer Networks

## Slide 2
Chapter 2 - Network Models

## Slide 3: Network Models
Networks require a combination of hardware and software to send data from one location to another
To make communications efficient
many components are involved, each with a specific function or service

## Slide 4
Layered Tasks
Hierarchy
 The complex task is broken into smaller subtasks
Services
 The higher layer uses the services of the lower layer

## Slide 5: Example of Sending a letter

## Slide 6: Postal Mail Example
Sender : Higher Layer, Middle Layer and Lower Layer
Carrier: Truck, train, airplane, boat or a combination thereof.
Receiver: Lower Layer, Middle Layer and Higher
Layer
Hierarchy: Tasks must be done in the order given in the hierarchy
Services: Each layer at the sending site uses the services of the layer immediately below it.

## Slide 7: Internet Model
Dominant model in data communications and networking
5 ordered layers; often referred to as TC P/IP protocol suite

## Slide 8: Peer-to-Peer Process

## Slide 9: OSI Layers

## Slide 10: OSI Layers

## Slide 11: Data Exchange Between Two Devices

## Slide 12: Physical layer

## Slide 13: Physical Layer Responsibilities
Physical characteristics of interfaces and media
– It defines the characteristic of the interface between devices and media. It also define the type of transmission media
Representation of bits
  The bit stream must be encoded into signals. It defines the type of representation ( how 0, 1 are changed to signal).
Data rate
  It defines the number of bits sent per second and also the d uration of bits
Synchronization of bits
  The sender and receiver must be use the same bit rate also the receiver clock must be synchronized

## Slide 14: Physical Layer Responsibilities
Line configuration
  Physical layer is concerned with the connection of devic es to the media ( point-to point or multipoint)
Physical topology
  How devices connected to make a network
  Devices can connected by using Star, mesh , bus, ring or hybrid topology
Transmission mode
  It defines the direction of transmission between two dev ices (simplex, half-duplex, or full duplex)

## Slide 15
The physical layer is responsible for transmitting individual bits from one node to the next.

## Slide 16: Data link layer

## Slide 17: Data Link Layer Responsibilities
Responsible for moving frames from one hop (node) to the next
Framing
  Divide the stream of bits received from network layer into data units called frames
Physical addressing
  Known also as the MAC or link address
  Data Link Layer adds a header to the frame to define the
  sender and receiver address of the frame.
  Ethernet uses 6-bytes (48-bits) physical address that imprinted on the NIC

## Slide 18: Data Link Layer Responsibilities
Flow control
  It imposes a flow control mechanism , if the data rate at the receiver is less than produced by sender the data link layer imposes a flow control to avoid overwhelming at the receiver
Error control
  Add mechanisms to detect and retransmit damaged or lost frames.
  Prevent also duplication of frames.
  Error control is normally achieved through a trailer added to the end of frame.
Access control
  When two or more devices are connected to the same link, data link layer protocols are necessary to determine which device has control over the link at given time

## Slide 19
The data link layer is responsible for transmitting frames from
one node to the next.
Note:

## Slide 20: Node-to-node delivery

## Slide 21: Example
In below figure a node with physical address 10 sends a frame to a node with physical address 87. The two nodes are connected by a link. At the data link level this frame contains physical addresses in the header. These are the only addresses needed. The rest of the header contains other information needed at this level. The trailer usually contains extra bits needed for error detection

## Slide 22: Network layer

## Slide 23: Network Layer Responsibilities
Responsible from the delivery of packets from the original source to the final destination across multiple networks
If two systems are connected to the same link, there is no need for network layer
Logical addressing
  Network layer adds unique ( IP or logical address) to the
packet.
  IP addresses are necessary for universal communications that are independent of physical network
  No two host address on the internet can have the same IP address
  IP addresses 32-bit address that uniquely define a host connected to the Internet

## Slide 24: Network Layer Responsibilities
Routing
  Provide the routing mechanism for the router which route the packet to their final destination.
  Routers: devices used when independent networks are connected to create an internetworking ( network of networks)

## Slide 25
The network layer is responsible for the delivery of packets from the original source to the
final destination.
Note:

## Slide 26: Source-to-destination delivery

## Slide 27: Source-to-destination delivery
In Figure 2.11 we want to send data from a node with network address A and physical address 10, located on one LAN, to a node with a network address P and physical address 95, located on another LAN. Because the two devices are located on different networks, we cannot use physical addresses only; the physical addresses only have local jurisdiction. What we need here are universal addresses that can pass through the LAN boundaries. The network (logical) addresses have this characteristic.

## Slide 28: Example 2
Figure 2.11

## Slide 29: Transport layer

## Slide 30: Transport Layer Responsibilities
The transport layer is responsible for the process-to-process delivery of the entire message. It ensures that the whole message arrives intact and in order, overseeing both error control and flow of control at the process-to-process level
The major duties of the transport layer are as follows:
Port addressing: The network layer gets each packet to the correct computer, the transport layer gets the entire message to the correct process on that computer using a port address.

## Slide 31: Transport Layer Responsibilities
Segmentation and reassembly: A message is divided in transmittable segments, each segment containing a sequence number. These numbers enable the transport layer to reassemble the message correctly upon arrival at the destination and to identify and replace packets that were lost in the transmission.
Connection control: The transport layer can be either connectionless or connection-oriented. A connectionless transport layer treats each segment as an independent packet and deliver it to the transport layer at the destination machine. A connection-oriented transport layer makes a connection with the transport layer at the destination machine first before delivering the packets. The connection is terminated once all packets are transferred.

## Slide 32: Transport Layer Responsibilities
Flow control: end-to-end flow control rather than across a single link as done in the data link layer.
Error control: end-to-end error control rather than across a single link as done in the data link layer.

## Slide 33
The transport layer is responsible for delivery of a message from one process to another.
Note:

## Slide 34
Reliable process-to-process delivery of a message

## Slide 35: Example 3
Figure shows an example of transport layer communication. Data coming from the upper layers have port addresses j and k (j is the address of the sending process, and k is the address of the receiving process).
Since the data size is larger than the network layer can handle, the data are split into two packets, each packet retaining the port addresses (j and k). Then in the network layer, network addresses (A and P) are added to each packet.

## Slide 36: Session Layer
It establishes, maintains and synchronize the interaction between communicating system
Monitors session identification so that only designated parties can participate
Examples: name lookup and user logon and logoff
  E.g., DNS name resolution, FTP’s logon/logoff
Function
  Dialog control
    Allows two systems to enter into dialog
    It allows the communication between two processes to take place in either half-duplex or full-duplex.
  Synchronization
    It allows a process to add checkpoints into a stream of data o So that if a failure of some sort occurs between checkpoints, the layer can retransmit all data since the last checkpoint.

## Slide 37: Presentation Layer
Concerned with the syntax and semantics of the information exchanged between two systems
Functions
  Translation
    At the sender it changes the information from its sender –dependent format into common format.
    At receiving, changes the common format into its receiver-dependent format
Encryption
  To ensure privacy and security
Compression
  Data compression reduces the number of bits contained in the information.
  It is important in the transmission of multimedia such as audio or video

## Slide 38: Application layer

## Slide 39: Application Layer Responsibilities
Set of interfaces to access networked services
Responsible for providing services to the user
  Mail services
    SMTP: Simple mail transfer protocol used to send electronic mail on the internet
  File transfer and access
    FTP : A protocol enable moving file across the network
  Remote log-in
    Telnet: A service that enables users on the intern et to log onto remote systems from their own hos t system
  Accessing the World Wide Web
    HTTP: Hyper text transfer protocol used for network file transfers in WWW environment

## Slide 40
The application layer is responsible for providing services to the user.
Note:

## Slide 41: Summary of duties

## Slide 42: OSI Model
Established in 1947, the International Standards Organization (ISO) is a multinational body dedicated to worldwide agreement on internati onal standards.
An ISO standard that covers all aspects of network communications is the Open Systems Int erconnection (OSI) model. (theoretical model f or networks of all kinds)
OSI reference model, drafted in late 1970s by
ISO
By 1983, the draft became ISO Standard 7498
  Common framework for developers and students of n etworking to work with and learn from
  Attempt to develop a working set of protocols and te chnologies based on the OSI model and to put those efforts into common use never materialized

## Slide 43: OSI Model
Networking can be separated into a series of related tasks
Each task can be conceptualized as a single layer, of the communication process
Reduces complexity of networked communications into series of interconnected tasks and activities
“Divide and conquer” approach: relationship a mong tasks persists, but each can be handled separately, and its issues solved independently
Reference models and standards enable intero perability among layers

## Slide 44: OSI Model

## Slide 45: Summary of OSI model

## Slide 46: TCP/IP and OSI model

## Slide 47: OSI vs TCP/IP
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application
Transport
Network
Data Link
Physical
Hardware
Firmware
Software
Operating System
User space
OSI
TCP/IP

## Slide 48
Some common data communications standards
Layer | Common Standards
5. Application layer | HTTP, HTML (Web) MPEG, H.323 (audio/video) IMAP, POP (e-mail)
4. Transport layer | TCP/UDP (Internet) SPX
3. Network layer | IP (Internet) IPX (Novell LANs)
2. Data link layer | Ethernet (LAN) PPP (dial-up via modem)
1. Physical layer | RS-232c cable (LAN) Category 5 twisted pair (LAN) V.92 (56 kbps modem)

## Slide 49
Some Protocols in TCP/IP Suite

## Slide 50
Thank You