## Slide 1: Data Communication and Computer Networks

## Slide 2: Chapter 3. Data and Signals

## Slide 3: Analog and Digital
To be transmitted, data must be transformed to electromagnetic signals
Data can be analog or digital. Analog data are continuous and take continuous values. Digital data have discrete states and take on discrete values.

## Slide 4: Analog and Digital Signals
Signals can be analog or digital form
Analog signals can have an infinite number of values in a range
digital signals can have only a limited number of values.

## Slide 5: Periodic and Non periodic Signals
Periodic – completes a pattern within a measurable time frame, called a period
  One full pattern is a cycle
  Analog signals
A periodic – changes without exhibiting a pattern
  Digital signals

## Slide 6: Periodic Analog Signals
Periodic analog signals can be classified as simple or composite.
A simple periodic analog signal, a sine wave, cannot be decomposed into simpler signals.
A composite periodic analog signal is composed of multiple sine waves
Sine wave is described by
  Amplitude
  Period (frequency)
  phase

## Slide 7: Amplitude
Absolute value of a signal’s highest intensity
Normally measured in volts

## Slide 8: Period
Period - amount of time to complete one cycle, expressed in
seconds (s)
Frequency – number of periods in one second, inverse of period

## Slide 9: Frequency
Rate of change with respect to time, expressed in hertz (Hz)
Change in a short span of time means high frequency
Change over a long span of time means low frequency

## Slide 10: Units of Period and Frequency

## Slide 11: Phase
Position of the waveform relative to time zero
Measured in degrees or radians

## Slide 12: Example 3.5
Express a period of 100 ms in microseconds, and express the corresponding frequency in kilohertz
From Table 3.1 we find the equivalent of 1 ms. We make the following substitutions:
100 ms = 100  10-3 s = 100  10-3  106 ms = 105 μs
Now we use the inverse relationship to find the frequency, changing hertz to kilohertz
100 ms = 100  10-3 s = 10-1 s f = 1/10-1 Hz = 10  10-3 KHz = 10-2 KHz

## Slide 13: Sine Wave Examples

## Slide 14: Example 3.6
A sine wave is offset one-sixth of a cycle with respect to time zero. What is its phase in degrees and radians?
We know that one complete cycle is 360 degrees.
Therefore, 1/6 cycle is
(1/6) 360 = 60 degrees = 60 x 2π /360 rad = 1.046 rad

## Slide 15: Wavelength
Another characteristic of a signal traveling through a transmission medium
Binds the period or the frequency of a simple sine wave to the propagation speed of the medium
Wavelength = propagation speed x period
= propagation speed/frequency

## Slide 16
A single frequency sine wave is not useful in data communications;
we need to send a composite signal, a signal made of many simple sine waves

## Slide 17: Composite Signals
A single-frequency sine wave is not useful in data communications; we need to send a composite signal, a signal made of many simple sine waves
When we change one or more characteristics of a single-frequency signal, it becomes a composite signal made of many frequencies
According to Fourier analysis, any composite signal is a combination of simple sine waves with different frequencies, phases, and amplitudes
If the composite signal is periodic, the decomposition gives a series of signals with discrete frequencies; if the composite signal is non periodic, the decomposition gives a combination of sine waves with continuous frequencies.

## Slide 18: Composite Periodic Signal

## Slide 19: Bandwidth
The bandwidth of a composite signal is the difference between the highest and the lowest frequencies contained in that signal
It is a measurement of how fast data can be sent over a wired or wireless connection, usually measure in bits per second.

## Slide 20: Signal Corruption

## Slide 21: Example 3.11
A signal has a bandwidth of 20 Hz. The highest frequency is 60 Hz. What is the lowest frequency? Draw the spectrum if the signal contains all integral frequencies of the same amplitude
B = fh - fl, 20 = 60 – fl, fl = 60 - 20 = 40 Hz

## Slide 22: Digital Signals
Information can also be represented by a digital signal. For example, a I can be encoded as a positive voltage and a 0 as zero voltage..
A digital signal can have more than two levels. In this case we can send more than 1 bit for each level

## Slide 23: Bit Rate and Bit Interval
Bit interval is the time required to send one single bit.
The bit rate is the number of bit intervals per second, i.e., the number of bits sent in one second. This is expressed as bps.
A digital signal with all its sudden changes, is actually a composite signal having an infinite number of frequencies.

## Slide 24: Example 3.18
Assume we need to download text documents at the rate of 100 pages per minute. What is the required bit rate of the channel?
Solution
A page is an average of 24 lines with 80 characters in each line. If we assume that one character requires 8 bits, the bit rate is

## Slide 25: Digital Signal as a Composite Analog Signal

## Slide 26: Transmission of Digital Signals
A digital signal is a composite analog signal with an infinite bandwidth
Baseband transmission: Sending a digital signal without changing into an analog signal

## Slide 27: Bandwidth Requirement
In baseband transmission, the required bandwidth is proportional to the bit rate; if we need to send bits faster, we need more bandwidth

## Slide 28: Broadband Transmission
Modulation allows us to use a bandpass channel
If the available channel is a bandpass channel, we cannot send the digital signal directly to the channel; we need to convert the digital signal to an analog signal before transmission.

## Slide 29: Modulation for Bandpass Channel

## Slide 30: Transmission Impairment

## Slide 31: Attenuation
Loss of energy to overcome the resistance of the medium: heat

## Slide 32: Distortion
The signal changes its form or shape
Each signal component in a composite signal has its own propagation speed
Differences in delay may cause a difference in phase

## Slide 33: Noise
Several types of noises, such as thermal noise, induced noise, crosstalk, and impulse noise, may corrupt the signal

## Slide 34: Signal-to-Noise Ratio (SNR)
To find the theoretical bit rate limit
SNR = average signal power/average noise power
SNRdB = 10 log10 SNR
Example 3.31: The power of a signal is 10 mW and the power of the noise is 1 μW; what are the values of SNR and SNRdB ?
Solution:

## Slide 35: Data Rate Limits
Data rate depends on three factors:
  Bandwidth available
  Level of the signals we use
  Quality of the channel (the noise level)
Noiseless channel: Nyquist Bit Rate
  Bit rate = 2 * Bandwidth * log2L
  Increasing the levels may cause the reliability of the system
Noisy channel: Shannon Capacity
  Capacity = Bandwidth * log2(1 + SNR)

## Slide 36: Nyquist Bit Rate: Examples
Consider a noiseless channel with a bandwidth of 3000 Hz transmitting a signal with two signal levels. The maximum bit rate can be calculated as
Bit Rate = 2  3000  log2 2 = 6000 bps
Consider the same noiseless channel, transmitting a signal with four signal levels (for each level, we send two bits). The maximum bit rate can be calculated as:
Bit Rate = 2 x 3000 x log2 4 = 12,000 bps

## Slide 37: Shannon Capacity: Examples
Consider an extremely noisy channel in which the value of the signal-to-noise ratio is almost zero. In other words, the noise is so strong that the signal is faint. For this channel the capacity is calculated as
C = B log2 (1 + SNR) = B log2 (1 + 0) = B log2 (1) = B  0 = 0
We can calculate the theoretical highest bit rate of a regular telephone line. A telephone line normally has a bandwidth of 3000 Hz (300 Hz to 3300 Hz). The signal-to-noise ratio is usually 3162. For this channel the capacity is calculated as
C = B log2 (1 + SNR) = 3000 log2 (1 + 3162) = 3000 log2 (3163)
C = 3000  11.62 = 34,860 bps

## Slide 38: Using Both Limits
The Shannon capacity gives us the upper limit; the Nyquist formula tells us how many signal levels we need.
Example: We have a channel with a 1 MHz bandwidth. The SNR for this channel is 63; what is the appropriate bit rate and signal level?
  First, we use the Shannon formula to find our upper limit
  C = B log2 (1 + SNR) = 106 log2 (1 + 63)
  = 106 log2 (64) = 6 Mbps
  Then we use the Nyquist formula to find the
  number of signal levels
  4 Mbps = 2  1 MHz  log2 L  L = 4

## Slide 39: Performance
Bandwidth (in two contexts)
  Bandwidth in hertz, refers to the range of frequencies in a composite signal or the range of frequencies that a channel can pass.
  Bandwidth in bits per second, refers to the speed of bit transmission in a channel or link.
Throughput
  Measurement of how fast we can actually send data through a network
Latency (Delay)
  Define how long it takes for an entire message to completely arrive at the destination from the time the first bit is sent out from the source
  Latency = propagation time + transmission time + queuing time + processing delay
  Propagation time = Distance/Propagation speed
  Transmission time = Message size/Bandwidth
Jitter error

## Slide 40
Thank you